## Slide 1
Congestion Management in Datacenter Networks:
Status Quo and Opportunities
Chen Tian（田臣）
Nanjing University

## Slide 2
Flow Control
Remote Flow Control
Congestion Control
Outline
Background
1
2
Our Thoughts
3
Our Work
4
Future Work

## Slide 3
Outline
Background
1
2
Our Thoughts
3
Our Work
4
Future Work

## Slide 4
DC Apps demand ultra-low latency
Background
Notes: new applications like storage on high I/O speed media, e.g. NVMe (non-volatile memory express) and large-scale machine learning training on high computation speed devices

## Slide 5
Latency costs!
Background
Amazon every 100ms of latency
Cost 1% in sales
The 100ms Rule
*data from https://akfpartners.com/growth-blog/what-is-latency
Google every 500ms of latency
Traffic drop 20%

## Slide 6
Average/tail both matter
Not only average latency, but also (maybe more important) tail latency
Background
Forward and backward propagation of Neural Network
Map-reduce task in Hadoop/spark system
Notes: 大数据系统Map-reduce，和机器学习系统中，一轮迭代需要依赖于所有流量的完成

## Slide 7
Compute
Network
Storage
Background
Network: new bottleneck (again)
NVM storage
μs-scale computation
Notes: (click) 存储介质在飞速发展，从HDD到SSD再到NVM非易失性存储介质不断涌现；
(click) 计算算力也在不断发展，从CPU到更加专用的GPU，DPU等； (click) 网络逐渐成为数据中心的瓶颈， 现在又出现存算分离场景，在此场景下，节点间通讯需求增加。
NVM：非易失性内存
Cite: Network Requirements for Resource Disaggregation (OSDI’16)
Jupiter Evolving: Transforming Google’s Datacenter Network via Optical Circuit Switches and Software-Defined Networking (SIGCOMM’22)
会议来自：SOSP, ASPLOS, FAST, HPCA等

## Slide 8
Why care congestion?
Background
Incast
Path collision

## Slide 9
What if uncontrolled?
Background
*Pic. from Congestion Control, SIGCOMM'22 Topic Preview
Notes: Cite: Congestion Control (SIGCOMM'22 Topic Preview)

## Slide 10: What we learn from textbook
TCP Slow start
Additive-increase/multiplicative-decrease (AIMD) rate adjusting
*pics from Computer Networking: A Top-Down Approach
Background

## Slide 11
DCN is far different from WAN!
Background
WAN (Wide area network)
Low per-conn bandwidth
Long distance
TCP/IP stack overhead
Heterogeneous devices
DCN (Datacenter Network)
High per-conn bandwidth
μs-scale propagation delay
Ultra-low delay on end-hosts (RDMA)
Regular topologies and devices
Environments
Low base RTT
Notes: DC regular的topo给了CC更多的设计空间，但是高链路带宽和传播时延也给CC带来了更大的需求

## Slide 12
DCN traffic pattern
Background
Bursty on-off traffic
Incast (many-to-one)
All-to-all
Client
Switch
Server
Server
Server
When congestion occurs (which is unavoidable and common), queuing delay dominate FCT of flows
Notes: 在数据中心中，流量的特征是突发式的潮汐流量，峰值负载很高；（click）且网络分布式的特点决定了多打一的incast流量模式是很常见的。
一方面数据中心提供了高带宽和基础的低时延，另一方面流量特征又使得网络的突发很常见；
（click）数据中心的这些特征共同使得流量在网络内的排队时延成为主导流量完成时间的关键因素。

## Slide 13
Congestion management
handle congestion to avoid collapse and provide good performance.
Including congestion control and flow control.
Background
when the receiver has no ability to receive…
flow control : solving the congestion on per-hop/endhost receiver entity
when too many senders sending too fast…
congestion control : solving the congestion in-network
Google Map：
Which route?
Or should not go out today?
Traffic light：
When to stop?
When to move?

## Slide 14
Challenges
Achieving low latency for small flows and tail network latency is not easy
Background
Low latency for small flows
Small queue occupancy
High bandwidth for large flows
Queue cannot be too small
*pics from Paydebt

## Slide 15
Outline
Background
1
2
Our Thoughts
3
Our Work
4
Future Work
Congestion Control
Flow Control
Intermediate zone

## Slide 16
Overview of state-of-the-art CM
Related works
Congestion Control
DCTCP, DCQCN, TIMELY, HPCC, Swift, PowerTCP, On-Ramp,
ExpressPass, pHost, Homa, NDP, Aeolus…
Flow Control
PFC, CBFC, BFC…
TCD

## Slide 17
Congestion Control
Related works
DCTCP, DCQCN, TIMELY, HPCC, Swift, PowerTCP, On-Ramp, …
React to congestion signals.
ExpressPass, pHost, Homa,
NDP, Aeolus, …
Use credits to schedule the transmission of packets.
Reactive
Congestion Control
Proactive
Congestion Control
Notes: At least one-RTT required before reaction.
Meets the first-RTT problem.

## Slide 18
Reactive Congestion Control (RCC)
Related works
  React to congestion signals AFTER congestion occurs.
  At least several RTTs are needed to converge.
data
ECN (DCTCP, DCQCN)
INT (HPCC)
RTT
(TIMELY, Swift)
Sender
Receiver
ACK

## Slide 19
ECN-based RCC
Related works
ECN based
e.g., DCTCP, DCQCN
*Congestion Control for Large-Scale RDMA Deployments. Yibo Zhu. SIGCOMM. 2015.

## Slide 20
RTT or INT based RCC
Related works
(Pic. from HPCC)
(Pic. from Swift)
delay based
e.g., Swift, TIMELY
INT based
e.g., HPCC, PowerTCP
*TIMELY: RTT-based Congestion Control for the Datacenter. Radhika Mittal. SIGCOMM. 2015.
Swift: Delay is Simple and Effective for Congestion Control in the Datacenter. Gautam Kumar. SIGCOMM. 2020.
*HPCC: high precision congestion control. Yuliang Li. SIGCOMM. 2019.

## Slide 21
Proactive Congestion Control (PCC)
Related works
  Schedule network transfer BEFORE sending.
  Usually transmit a portion of unscheduled packets before bandwidth allocation, which also induces bursts.
Sch
Token allocation
(Homa, ExpressPass, NDP)
Sender
Receiver
Token
Unsch
NOTE: We could use Token-based CC and Proactive CC alternately in our following slides.

## Slide 22
Pure PCC: ExpressPass
Related works
  Promise 1: near-zero queue
  Promise 2: zero packet loss
  Promise 3: fast convergence
(Pic. from ExpressPass)
*Credit-Scheduled Delay-Bounded Congestion Control for Datacenters. Inho Cho. SIGCOMM. 2017.

## Slide 23
Waste of the first-RTT hurts
Related works
Most flows (w/o congestion) could have been finished within the first RTT!
(Pic. from Aeolus)
(Pic. from TCC, Memcached, 100 Gbps)

## Slide 24
Homa
Related works
  Scheduled: adaptive priority
  Unscheduled: priority thresholds
  Unscheduled: higher priorities
(Pic. from Homa)
*Homa: a receiver-driven low-latency transport protocol using network priorities. Behnam Montazeri. SIGCOMM. 2018.

## Slide 25
NDP
Related works
  Packet trimming → deterministic packet loss
  Receiver-driven packets pulling
Sender
Receiver
Pull
Payload trimming
Payload
Header
*Re-architecting datacenter networks and stacks for low latency and high performance. Mark Handley. SIGCOMM. 2017.

## Slide 26
Aeolus
Related works
  A patch to PCC
  Send unscheduled packets at the first RTT aggressively
  selectively drop unscheduled
(Pic. from Aeolus)
*Aeolus: A Building Block for Proactive Transport in Datacenters. Shuihai Hu. SIGCOMM. 2020.

## Slide 27
Aggressive injection may not help
Related works
To send unscheduled, or not to be, that is the question.
(Pic. from Paydebt)

## Slide 28
Can FC address 1st RTT dilemma?
Related works
  FC can ensure that buffer does not overflow
    ≠ a good application level performance (e.g., FCT)
  Side effects are:
    Congestion spreading
    HOL-blocking -> victim flow problem
    …
Notes: 这张图：大车（non-incast）和小车(incast)混合在一起控制

## Slide 29
PFC (FC in Ethernet)
Related works
HOL-blocking, congestion spreading and deadlock.
Pause an upstream port if the ingress queue length exceeds a threshold.
Operates at a per-port granularity.
(Pic. from TCD, sigcomm21)
*IEEE 802.1 Qbb - Priority-based Flow Control. http://www.ieee802.org/1/ pages/802.1bb.html. 2010.

## Slide 30
Related works
The downstream switch sends a Flow Control Credit Limit (FCCL) message to the upstream switch periodically.
The upstream switch uses FCCL to calculate the number of credits.
(Pic. from TCD, sigcomm21)
Still could not avoid HOL blocking.
CBFC (FC in Infiniband)
*InfiniBandTM Architecture Specification Volume 1 Release 1.4. https://cw.infinibandta.org/document/dl/8567. InfiniBand Trade Association. 2020.

## Slide 31
Related works
  Flows are assigned to 32-128 queues per port according to <flow-ids, hash>.
  A flow is assigned to an empty queue if possible and could share with other flows when all queues are occupied.
  HOL blocking still occurs when different flows share the same queue.
BFC
*Backpressure Flow Control. Prateesh Goyal. NSDI. 2022.

## Slide 32
Related works
  Current CC and FC are incompatible
    The on-off control of FC could influence the congestion detection of CC
    Introduce a third state “undetermined” to avoid sending rate reduction by CC on senders
Intermediate zone - TCD
Does not address HOL blocking caused by FC itself
*Congestion Detection in Lossless Network. Yiran Zhang. SIGCOMM. 2021.

## Slide 33
Outline
Background
1
2
Our Thoughts
3
Our Work
4
Future Work
Trends in DC
Our vision

## Slide 34
Several trends in datacenter
Related works
BDP is now 10-100x higher (due to link speed)
  More flows could finish transmitting within the first BDP (before CC even steps in).
(Pic. from FS community)
(Pic. from Aeolus)

## Slide 35
Several trends in datacenter
Related works
Datacenter is now hyperscale (up to 2,600,000 servers)
  Incast scale can be 10-100x.
(Pic. from servertech)

## Slide 36
Related works
Switches’ relative buffering capacity is decreasing
Several trends in datacenter
(Pic. extended from BFC)
CC Alone is not effective!

## Slide 37
Our vision
Revisiting existing solutions
Strong CC to handle congestion
Congestion Control
DCTCP, DCQCN, TIMELY, HPCC, Swift, PowerTCP, On-Ramp,
ExpressPass, pHost, Homa, NDP, Aeolus…
Relatively “weak” FC to avoid buffer overflow
Flow Control
PFC, CBFC, BFC…
TCD

## Slide 38: Times have changed
Our vision

## Slide 39: Role diff between CC & FC
Flow Control：Already injected packets
CC&FC Boundary
Congestion Control：Not yet injected packets

## Slide 40
Our vision
Our vision
Relatively “weak” CC to handle persistent congestion
Strong FC to handle transient congestion
Low latency
High throughput
Convergence
Fairness
Control different traffic (e.g., congested/non-congested) separately

## Slide 41
Outline
Background
1
2
Our Thoughts
3
Our Work
4
Future Work
Flow Control
Remote Flow Control
Congestion Control

## Slide 42
Outline
Background
1
2
Our Thoughts
3
Our Work
4
Future Work
Flow Control
Remote Flow Control
Congestion Control

## Slide 43: DCQCN+ Overview
Motivation
  DCQCN cannot suppress an incast congestion when its number of flows exceeds hundreds.
DCQCN+ Design
  Congestion scale detection
  Dynamic parameters
  New increase patterns
Performance
  At least 10x larger scale with 20x smaller queue length
  >90% throughput improvement
Adopted in RDMA adapters & ICNP’18
*DCQCN+: Taming Large-Scale Incast Congestion in RDMA over Ethernet Networks. ICNP. 2018.

## Slide 44: TOP Overview
Motivation
  Qos-support is missing in proactive CC field.
TOP Design
  In-network prioritization on tokens
  Bounded queue
  Credit feedback control
Performance
  Reduce the average FCT and tail latency by 80-90%, especially for small flows.
TPDS’20
*Exploring Token-oriented In-network Prioritization in Datacenter Networks. TPDS. 2020.

## Slide 45: ToCC Overview
Motivation
  There lacks of systematic exploration of the TCC (token-based congestion control) design space
Contributions
  A framework of TCC
  Devise a protocol ToCC upon the framework
  Implement ToCC in NP-based NICs
Performance
  Flexible for higher bandwidth links
  Robust for incast scenarios
  Benefits small flows by achieving a small queue length as well as benefiting large flows by obtaining stable high throughput
*An Anatomy of Token-based Congestion Control.. TON. 2025.

## Slide 46: Paydebt Overview
Motivation
  Existing TCC struggles with the transmission of the first RTT
Paydebt Design
  Debt mechanism to paying back the unallocated bandwidth
  A suitable congestion control algorithm for TCC
Performance
  Reduce the FCTs of small flows by 50.2% - 85.4%
  Reduce the FCTs of all flows by 13.0% - 38.1%
TPDS’22
token
sch
debt
unsch
*PayDebt: Reduce Buffer Occupancy Under Bursty Traffic on Large Clusters. TPDS. 2022.

## Slide 47: PrioPlus’s Key Concept: Delay Channel
PrioPlus assigns specific delay ranges, termed as channels, to each priority.
Delay
Delay channel of this priority
Delay channel of the higher priority
Delay channel of the lower priority
*Enabling Virtual Priority in Data Center Congestion Control. Eurosys. 2025 (best student paper).

## Slide 48: (Re)Discovery of the New World

## Slide 49
Outline
Background
1
2
Our Thoughts
3
Our Work
4
Future Work
Flow Control
Remote Flow Control
Congestion Control
Our work

## Slide 50
P-PFC Overview
Our work
Motivation
  In PFC, An upstream port may receive PFC PAUSE continuously during the congestion phase, leading to cascading PFC pauses in upstream switches
P-PFC Design
  Predict the occurrence of congestion, pausing the upstream before the queue length build up.
Performance
  Reduce the maximum queue length and tail latency by 4x and 2x under high and low pressure, respectively.
TPDS’20
*P-PFC: Reducing Tail Latency with Predictive PFC in Lossless Data Center Networks. TPDS. 2020
Notes: 两个关键发现：
在网络拥塞时上游端口可能连续收到PAUSE信号，这会导致上游的级联暂停
交换机可以通过检测当前buffer的变化趋势来预测未来拥塞的产生

## Slide 51: Floodgate Overview
Motivation
  Incasts hurt flows’ performance, at the same time unavoidable.
Floodgate Design
  A per-hop flow control that is compatible with state-of-the-art CC
  A sending window to identify and control the transmission of incast flows
  Leverage VOQ to isolate incast flows
Performance
  Reduce the average FCTs (10.1% ~ 98.1%), as well as the 99th-tail latency (1.1 ～ 207x) under incast mixed with Possion arrival flows scenarios.
  Reduce the maximum buffer occupancy by a factor of 6.6x.
CoNEXT’21
*Floodgate: Taming Incast in Datacenter Networks. CoNEXT. 2021.

## Slide 52: Pyrrha Overview
Motivation
  There are different types of congestion in networks (e.g., incast, load imbalance)
  Transient congestion can not be avoided, instead, the negative effects of it should be eliminated.
Pyrrha Design
  A congestion-root based flow control that is compatible with state-of-the-art CC
Performance
  The average FCT of uncongested flows is reduced by 42.8%-98.2%, and 99th-tail latency can be 1.6×-215× lower, without compromising the performance of congested flows
  Reduce the maximum buffer occupancy by up to 1.8×-6.2×
NSDI’25
* Pyrrha: Congestion-Root-Based Flow Control to Eliminate Head-of-Line Blocking in Datacenter. NSDI. 2025.

## Slide 53
Outline
Background
1
2
Our Thoughts
3
Our Work
4
Future Work
Flow Control
Remote Flow Control
Congestion Control
Our work

## Slide 54: SWING Overview
Motivation
  2022 年 2 月，China initiated 东数西算工程 (East Data, West Compute)
  Long distance links bring
    Large RTT delays the network signals (e.g., congestion signal, packet loss)
    Large BDP requires deep buffer on DCI switch and increases queueing delay
SWING Design
  Decouple packets buffer and FC signal trigger
    A shallow buffer for intra-DC to trigger FC signal
    A deep buffer for inter-DC to accommodate in-flight packets
  Decouple the inter-DC and intra-DC management
  FC signal can be triggered fast
Performance
  Reduce the average FCT for inter-datacenter traffic by 14% - 66%
TPDS’23
*SWING: Providing Long-Range Lossless RDMA via PFC-Relay. TPDS. 2023.

## Slide 55: Bifrost Overview
PFC is myopic
  PFC does not know how many packets are in-flight
  PFC merely focuses on queue length to make control decisions
Biofrost Design
  Insights: If the downstream records what frames have been sent, it knows exactly how many packets are in-flight
Performance
  Improve the performance of small flows
ICNP’23
*Bifrost: Extending RoCE for Long Distance Inter-DC Links. ICNP/TON. 2023.

## Slide 56: BifrostX Overview
Multiple priorities
TON accepted
个优先级对应的令牌
个总令牌

## Slide 57
Outline
Background
1
2
Our Thoughts
3
Our Work
4
Future Work

## Slide 58: DCN in AI computing
Model Parallel
Data Parallel
Pipeline Parallel
Collective communication

## Slide 59: Vertical: cross boundaries
The destination of network…
IO，
architecture，
system…
Future Work

## Slide 60: Horizontal：scales
Inter-nodes
Intra-nodes
Cross-dc
Future Work

## Slide 61
Future Work
Long distance (e.g., inter-DC)
App-oriented
New architecture
(e.g., Universal Bus)
Lossy…
RDMA multicast
Universal FC CC protocols…
Future Work

## Slide 62: Take home idea
The time of
Flow Control is coming!
Future Work

## Slide 63: Pyrrha: Congestion-Root-Based Flow Control to Eliminate Head-of-Line Blocking in Datacenter
Kexin Liu*, Zhaochen Zhang*, Chang Liu, Yizhi Wang, Vamsi Addanki, Stefan Schmid, Qingyue Wang, Wei Chen, Xiaoliang Wang, Jiaqi Zheng, Wenhao Sun, Tao Wu, Ke Meng, Fei Chen, Weiguang Wang, Bingyang Liu, Wanchun Dou, Guihai Chen, Chen Tian
Notes: Hello everyone, this is ________ from Nanjing University.
Today, I am delighted to share with you Pyrrha, which is focused on managing transient congestion using scalable and head-of-line-blocking-free flow control.

## Slide 64: Due to VISA issue...
Kexin Liu
Receives her Ph.D. Degree at 2023. Her research interests include congestion management in Datacenter and building network stack for AI clusters.
She is now a senior research engineer in Huawei.
Zhaochen Zhang
He is a Ph.D. candidate from Nanjing University. His research interests focus on the transport layer in data center, including congestion management, and reliable transmission.
He is planning to graduate in 2026 and is in the job market.
Notes: Due to visa issues, both co-first authors of this paper are unable to attend NSDI, so I am presenting on their behalf.
Firstly, let me provide some background information.

## Slide 65: CC is Falling for Transient Congestion
Trend1: The high port bandwidth allows sending out more flows within
the first RTT, even before congestion control could step in.
Figure source: Harmony@NSDI '24
Flow Size (Bytes)
Notes: With data center networks evolving, there are three trends making congestion control increasingly struggle to manage transient congestion.
The first trend is that as port bandwidth grows, more and more flows can be sent out in the first RTT. Since most congestion controls require one RTT to receive the congestion signal, they cannot manage the transient congestion caused by the first RTT traffic.

## Slide 66: CC is Falling for Transient Congestion
Trend2: The growing scale of DCN and the emerging workloads (e.g., distributed training) lead to more bursty traffic.
Figure source: HPN@Sigcomm ‘24
Notes: The second trend is that the increasing scale of data center networks and the emergence of workloads such as distributed training will result in more bursty traffic, which means more transient congestion.
// For example, a paper from Alibaba reports its training data center will have fifteen thousand NICs in a pod. And the traffic pattern of each NIC is periodic bursts. This trend may lead to more frequent and larger-scale transient congestion.

## Slide 67: CC is Falling for Transient Congestion
Trend3: The decreasing buffer-to-bandwidth ratio calls for faster congestion management for transient congestion.
Figure source: PrioPlus@EuroSys ‘25
Notes: The third trend that makes the situation worse is the decreasing buffer-to-bandwidth ratio, which significantly reduces switches’ ability to absorb transient congestion.

## Slide 68: CC is Falling for Transient Congestion
Trend3: The decreasing buffer-to-bandwidth ratio calls for faster congestion management for transient congestion.
Figure source: PrioPlus@EuroSys ‘25
Data center networks need to manage transient congestion more quickly.
Notes: These three trends together demand that data center networks should have an enhanced ability to manage transient congestion more quickly.

## Slide 69: Our Vision for Data Center Congestion Management
Per-hop FC handles transient congestion.
Sender
Receiver
Switch
Switch
End-to-end
Congestion
Control
CC signals
FC frames
Per-hop Flow Management
End-to-end CC handles persistent congestion.
Notes: To solve the transient congestion problem, our vision
⊕ is to leverage per-hop flow control to handle transient congestion.
When applying per-hop flow control, a switch can manage congestion using control frames within a one-hop transmission delay of around one microsecond.
// It is in a unique position to quickly manage flows that have already been injected into the network to avoid performance downgrades.
⊕ And traditional congestion control could be used to adjust flow rates at the end host to avoid persistent congestion.
This labor division between congestion control and per-hop flow control leverages their unique positions to collaboratively manage data center congestion. We will later demonstrate the effectiveness of this division. Next, let’s explore the drawbacks of existing per-hop flow controls.
// Note that later in the presentation, we will use the terms "per-hop flow control" and "flow control" interchangeably.

## Slide 70: HOL Blocking Problem of Naive FC
Head-of-Line Blocking: a flow is paused innocently by the congested port that it does not pass through.
Congested port
Vulnerable flows
Congested flows
P3
P4
P2
P1
Paused
port
Uncongested port
Pause
HOL Blocking!
Queue at P3 in PFC
Paused!
Blocked!
Notes: Naive flow control like PFC is widely used to avoid buffer overflow in the RoCEv2 network. However, PFC is well-known for incurring head-of-line blocking, a performance killer in RoCEv2.
Let’s use the scenario shown on the screen as an example to introduce head-of-line blocking in detail. In this scenario, multiple congested flows intersect at port P2,
⊕ causing congestion and triggering PFC to pause P3 and P4.
⊕ Let's assume another vulnerable flow
⊕ shares the same queue with the congested flow on P3 and then passes P1.
⊕ Although this flow does not pass the congested port and allowing it to send will not cause buffer overflow, it will also be paused innocently, which is called head-of-line blocking. // When ingress queue length exceeds a threshold, PFC pauses the upstream in per-priority-queue granularity. PFC is well-known for incurring head-of-line blocking, a performance killer in RoCEv2.

## Slide 71: HOL Blocking Problem of Naive FC
Test workload:
continuous incast flows
Receiver
Notes: To demonstrate the impact of head-of-line blocking on performance, we conduct a simulation in a fat-tree topology.
The test workload consists of three types of flows. Incast flows start at the beginning of the simulation, in which all other hosts send small flows to the last host in the topology, making the last pod congested.

## Slide 72: HOL Blocking Problem of Naive FC
Receiver
Test workload:
continuous incast flows +
vulnerable flows with a total rate of 80 Gbps
Notes: Vulnerable flows are flows sent from other pods to other hosts in the last pods with the total rate being eighty gigabits per second. These flows may suffer from head-of-line blocking at destination aggregation switches and core switches.

## Slide 73: HOL Blocking Problem of Naive FC
Test workload:
continuous incast flows +
vulnerable flows with a total rate of 80 Gbps +
background flows with a total rate of 80 Gbps
Notes: And background flows are sent between uncongested pods with the total rate being eighty gigabits per second. These flows could also be blocked if congestion is not properly controlled and spread to other pods.

## Slide 74: HOL Blocking Problem of Naive FC
PFC: The throughput of vulnerable flows and background flows is severely hurt due to HOL blocking.
Notes: The result of PFC is shown on the screen.
⊕ During the first two microseconds, vulnerable flows are significantly blocked.
⊕ Between the first and second microsecond, congestion spreads to all of the pods, blocking background flows.
This result reveals that head-of-line blocking incurred by PFC significantly impacts the transmission of uncongested flows. Additionally, CBFC performs similarly to PFC, as they both control transmission at the granularity of the entire queue.

## Slide 75: Idealized FC can Eliminate HOL blocking but is Non-scalable
Per-flow-queue FC: Vulnerable and background flows fully utilize the link, at the same time the throughput of incast flows does not downgrade.
Not scalable: There could be thousands of flows that can be observed on a port [1,2].
[1] (EuroSys18) Information rich flow record generation on commodity switches.
[2] (SigMetric24) Lightweight Acquisition and Ranging of Flows in the Data Plane.
Notes: To overcome the head-of-line blocking caused by coarse-grained control, an idealized way is per-flow queue flow control, where only queues assigned to congested flows are paused and uncongested flows are unaffected.
⊕ However, this solution is not scalable as there could be thousands of flows observed on a port.

## Slide 76: State-of-the-art FC is Flawed
BFC@NSDI22: Vulnerable and background flows sharing the same queue with incast flows are severely hurt.
Notes: BFC, the state-of-the-art flow control, attempts to mimic per-flow-queue using a limited number of queues. When the number of active flows exceeds the number of queues, the remaining flows are randomly assigned to the already-used queues.
⊕ As shown in the figure, although many uncongested flows complete quickly, some flows take a long time because they randomly share queues with congested flows and suffer from head-of-line blocking.

## Slide 77: State-of-the-art FC is Flawed
BFC@NSDI22: Vulnerable and background flows sharing the same queue with incast flows are severely hurt.
How to eliminate HOL blocking caused by
flow control in the most cost-effective way
Notes: Given this situation, we raise the question:
How to eliminate head-of-line blocking caused by flow control in the most cost-effective way?

## Slide 78: We Need a Better Control Granularity for Per-hop FC
PFC’s control granularity:
control the entire priority queue.
Head-of-line blocking.
Per-flow-queue’s control granularity: control at the flow granularity.
Non-scalable.
A better control granularity?
Blocking-free and scalable.
Notes: Reviewing existing per-hop flow control protocols, we find that the key is control granularity. A coarse control granularity can lead to head-of-line blocking, while overly fine granularity can result in excessive resource consumption, making it non-scalable. Therefore, we need to find a better control granularity.

## Slide 79: Analysis of Congestion in Per-hop FC
P3
P4
P1
P2
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P5
Pause
Pause
Notes: Our analysis begins with the congestion in per-hop flow control, which is illustrated through this example.
In the example,
⊕ Five flows intersect at P2, causing congestion,
⊕ which then triggers pauses to P3, P4, and P5. As flows continue to transmit,
⊕ the queue lengths at P3, P4, and P5 increase, leading to pauses to upstream ports.

## Slide 80: Analysis of Congestion in Per-hop FC
P1
P3
P4
P2
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P5
Congestion Tree
Congestion Root
Notes: Analyzing the ports involved in this congestion event, we found they naturally form a tree structure. Only the congestion at P2 is unavoidable, and the congestion at other ports is triggered by pauses from P2.
⊕ Therefore, P2 is both the root of the tree structure and the root cause of the congestion, referred to as the congestion root.
// Ports that are both paused by the congestion root and pause other ports are called hotspots, while ports that are paused but do not pause any upstream ports are called leaves.

## Slide 81: Analysis of Congestion in Per-hop FC
Key insight: Congestion root is the appropriate granularity of flow control!
Only control the flows passing through the congestion root.
Blocking-free.
The number of concurrent congestion roots observed on each port is moderate [3].
Scalable.
[3] (IMC) Network traffic characteristics of data centers in the wild.
Notes: Since the congestion root is the root cause of congestion, the flows contributing to it form the minimal set that must be controlled. By only controlling these flows, other flows will not be blocked.
⊕ And the number of concurrent congestion roots observed on each port is moderate. Therefore, only a reasonably small amount of resources is required at each port, making the flow control scalable.
⊕ According to our analysis, we conclude the key insight of this work: congestion root is the appropriate granularity of flow control to achieve both blocking-free and scalable.

## Slide 82: Pyrrha: A Congestion-Root-Based Flow Control
P3
P4
P1
P2
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P5
Pause
Pause
Isolation queue (IQ) for root P5
Default output queue (OQ)
Queue allocation at P3
Notes: Based on the insight, we propose Pyrrha, a congestion-root-based per-hop flow control protocol.
Specifically, the Pyrrha switch will embed the congestion root ID in the pause frame. Upon receiving a pause frame, the upstream Pyrrha switch allocates an isolation queue dedicated to the congestion root. Then traffic passing through the congestion root is placed into the isolation queue. Traffic that does not pass through the congestion root remains unaffected by the congestion.

## Slide 83: Pyrrha: A Congestion-Root-Based Flow Control
P3
P4
P1
P2
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P5
Pause
Pause
Isolation queue (IQ) for root P5
Default output queue (OQ)
Queue allocation at P3
Pyrrha is a HOL-blocking free per-hop FC protocol requiring the minimal number of queues.
（formally proven in the technical report released with our paper.)
Notes: By leveraging congestion root as the control granularity, Pyrrha can be formally proven as a head-of-line-blocking-free flow control protocol requiring minimal queues. Please see the technical report released together with our paper for the formal proof.
However, to realize congestion root-based flow control, there are some challenges to be solved.

## Slide 84: Key Challenge: Identify Congestion Root
P3
P4
P1
P2
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P5
HOL Blocking!
Notes: The first challenge as well as the key challenge is identifying the congestion root accurately.
This is difficult in practice because upstream non-root hotspots can become congested before the actual congestion root. For example,
⊕ non-root port P3 might be congested first, and pause flows passing through it.
⊕ However, the true congestion root is P2.
⊕ If Pyrrha cannot converge to recognize P2 as the root, it can cause head-of-line blocking for the vulnerable flow that does not pass through P2.

## Slide 85: Pyrrha Design: Distributed Congestion Root Election
P3
P4
P1
P2
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P5
Default output queue (OQ)
Queues at P3
I am the root!
Pause
P6
Notes: Inspired by the Spanning Tree Protocol, Pyrrha proposes a distributed congestion root election mechanism. This approach is based on the fact that congestion roots are always downstream, which ensures accurate root identification.
We use the following example to illustrate the process of distributed root election.
⊕ When there is no congestion, all flows are enqueued into the port's output queue.
⊕ If the output queue length exceeds the congestion threshold,
⊕ the port claims itself as the root and sends pause frames with its port ID upstream.

## Slide 86: Pyrrha Design: Distributed Congestion Root Election
I am the root!
P3
P4
P1
P2
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P5
Default output queue (OQ)
Queues at P6
Pause
P6
Isolation queue (IQ) for root P3
Notes: Upon receiving the pause frame,
⊕ the upstream port assigns an IQ dedicated to the congestion root
⊕ and enqueues the flow passing through the congestion root into the IQ.

## Slide 87: Pyrrha Design: Distributed Congestion Root Election
P3
P4
P1
P2
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P5
I am the root!
I am the root!
Pause
Pause
P6
Notes: When the downstream port P2 also experiences congestion, it identifies itself as the congestion root
⊕ and sends pause frames with its ID to the upstream ports.

## Slide 88: Pyrrha Design: Distributed Congestion Root Election
P3
P4
P1
P2
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P5
I am the root!
Merge
Pause
P2 is the root!
P6
Notes: Upon receiving this pause frame, the upstream port P3 relinquishes and recognizes P5 as the new congestion root.
After a new root is elected, Pyrrha merges the old congestion tree into the new one.
⊕ This process is achieved by sending Merge frames from the false-positive root P3 to upstream ports. When P6 receives the merge frame, it cancels the IQ assigned to P3, allowing the vulnerable flow to be free of the blocking.
After the actual congestion root arises, the congestion root election and merge process finishes within several link delays. Therefore, false-positive congestion roots have a minimal impact on performance.

## Slide 89: Challenge 2: Identify Congested Flows
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P3
P4
P1
P2
P5
Will the new flow pass through
the congestion root P2？
P6
P7
Notes: The second challenge is identifying congested flows.
Pyrrha actively identifies and controls congested flows rather than passively reacting after they reach the congestion root.
⊕ This approach prevents additional pressure from being placed on the congestion root by new flows.
⊕ To determine whether a flow will pass through the congestion root, the Pyrrha switch needs to identify the onward path of each flow.
This is challenging as various load balancing protocols may be applied in data centers, which can complicate determining the path of packets.

## Slide 90: Challenge 2: Identify Congested Flows
In data centers, various load balancing protocols may be applied, which can complicate determining the path of data packets.
ECMP
Source routing
Packet spraying
CONGA (Sigcomm14)
FlowBender (Sigcomm14)
ConWeave (Sigcomm23)
PLB (Sigcomm22)
LetFlow (NSDI17)
DRILL (Sigcomm17)
Notes: This is challenging as various load balancing protocols may be applied in data centers, which can complicate determining the path of packets.

## Slide 91: Design 2: Hash-aware Path Calculation
In data centers, LB protocols can be categorized into three types, all of which are compatible with Pyrrha.
ECMP
Source routing
Packet spraying
CONGA (Sigcomm14)
FlowBender (Sigcomm14)
ConWeave (Sigcomm23)
PLB (Sigcomm22)
DRILL (Sigcomm17)
Path information is directly embedded in the packet header
Path is calculated through hash function at each hop
Please see our paper for how Pyrrha work with dynamic LB protocols.
Notes: In data centers, LB protocols can be categorized into three types,
⊕ The first type of LB protocols directly embeds path information into the packet header, //such as source routing or CONGA.
These routing protocols naturally compatible with Pyrrha.
⊕ The second type uses a hash function to calculate the forwarding path at each hop, like ECMP// or FlowBender.
For this type of LB, we propose an efficient hash-aware path calculation method to determine paths on switch, which will be detailed next.
⊕ For dynamic LB protocols which have unpredictable paths, Pyrrha can still work with it on the downlinks in a clos topology. Please refer to our paper for details.

## Slide 92: Design 2: Hash-aware Path Calculation
Challenge: To determine the path of a packet, a switch must know the hash results of other switches.
[4] (FAST05) A scalable and high performance software iscsi implementation.
[5] (ATC22) Hashing design in modern networks: Challenges and mitigation techniques.
Our finding: Current switches only provide a limited number of hash functions to prevent complex hashing from impeding forwarding rates [4,5].
Our solution: Only store the hash function types and hash seeds used by other switches to calculate the hash results.
Notes: For hash-based LB protocols, the challenge in calculating path is that a switch must know the hash results of other switches.
⊕ By leveraging the finding that current switches only provide a limited number of hash functions to prevent complex hashing from impeding forwarding rates,
⊕ Pyrrha switch only needs to store the hash function types and hash seeds used by other switches to calculate the hash results.

## Slide 93: Challenge 3: Handle Tree-tangling Scenarios
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P4
P5
P1
P2
P6
P3
P8
P9
P7
Notes: The third challenge is handling tree-tangling scenarios.
Several concurrent congestion trees can be intertwined among themselves. As an example, after a congestion tree forms with P2 as the root,
⊕ two additional flows from P8 and P9 are sent to P6 and then pass through P3.
⊕ The new flows, which are not part of the congestion tree rooted at P2, will cause P6’s OQ congestion, prompting P6 to declare itself the root and pause these flows.
In this case, two congestion trees tangle with each other.

## Slide 94: Challenge 3: Handle Tree-tangling Scenarios
P8
P9
P3
P1
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P4
P5
P2
P6
Congestion Tree rooted at P2
P7
Notes: The first is the congestion tree rooted at P5

## Slide 95: Challenge 3: Handle Tree-tangling Scenarios
P3
P4
P5
P1
P2
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P6
P8
P9
P7
Congestion Tree rooted at P6
Notes: And the second is the congestion tree rooted at P6

## Slide 96: Challenge 3: Handle Tree-tangling Scenarios
P1
P3
P4
P5
Tree-tangling
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P2
P6
P8
P9
P7
Notes: This results in P6 being both a hotspot and a congestion root, and the flow sent from P7 passes through two congestion roots, posing challenges for the flow control mechanism.

## Slide 97: Challenge 3: Handle Tree-tangling Scenarios
P1
P3
P4
P5
Tree-tangling
Root
Hotspot
Leaf
Vulnerable flows
Congested flows
P2
P6
P8
P9
P7
Please see our paper for how Pyrrha identifies congestion flows and handles tree-tangling scenarios.
Notes: For reasons of time, we omit Pyrrha’s design on the last two challenges. Please see our paper for details.

## Slide 98: Pyrrha’s Prototype
We implement a Pyrrha prototype on Tofino2 with 2.5k lines of P4 code and 2k lines of Python code.
Notes: Pyrrha is implementable. We implement a Pyrrha prototype on Tofino2.

## Slide 99: Pyrrha’s Prototype: Optimization
The multiple equal path and up-down routing properties of typical data center topologies are leveraged to enable Pyrrha to calculate paths for a topology with 11,664 hosts (fat-tree with k=36) using just 440 KB of storage.

## Slide 100: Pyrrha’s Prototype: Optimization
An innovative Multi-segment QueueID Stack is used, allowing one-pass allocation and freeing of queues within Tofino2's pipeline architecture.

## Slide 101: Pyrrha’s Prototype: Compromise
Queue state tables require storage This overhead is unoptimizable due to Tofino2's pipeline architecture, consuming 8.64MB of storage in an 11,664 hosts (fat-tree with k=36) topology.

## Slide 102: The Overhead of Pyrrha’s Prototype
Our Pyrrha prototype can easily scale to a k=36 fat-tree topology (≈11k hosts), with around 11 MB (44.5% of Tofino2) memory resource consumption.
Notes: With careful optimizations, it requires only forty percent of Tofino2 memory resources to support around ten thousand hosts.

## Slide 103: Testbed Evaluation
Pyrrha significantly reduces the FCT of vulnerable flows compared with PFC.
Topology: 2-stage clos topology with 2 cores and 3 ToRs.
Workload: Web Server and Web Search.
Notes: We tested the performance of the Pyrrha prototype in a two-stage Clos topology where all switches are running Pyrrha. Under both web server and web search workloads, Pyrrha significantly reduced the FCT compared with PFC.

## Slide 104: Simulation Evaluation
FCT in incast-mix scenario, compare with other FCs
Topology: 2-stage clos topology with 160 hosts.
Incast flows: periodically generated with average load at 0.5.
Vulnerable and background flows: generated following Poisson process with load at 0.8.
~200x
~30x
Basically the same
Notes: Next, we give some simulation evaluation results on Pyrrha.
In a simulation with a one-hundred-and-sixty host topology, compared with other flow control protocols,
⊕ Pyrrha improves the performance of vulnerable and background flows significantly,
⊕ without compromising the performance of congested flows.

## Slide 105: Simulation Evaluation
FCT in incast-mix scenario, with or without CC
Pyrrha significantly benefits uncongested flows compare with pure CC solution.
Pyrrha can cooperate with existing CC to achieve better performance for small flows.
~150x
~20x
~2x
~2x
Notes: Compared with a pure congestion control solution,
⊕ Pyrrha also significantly benefits vulnerable and background flows without compromising congested flows.
⊕ When Pyrrha cooperates with congestion control, the performance of small flows is further improved.

## Slide 106: Simulation Evaluation
Pyrrha’s queue usage is moderate
Topology: standard fat-tree with k=16 (1024 hosts).
Most stressful workload: (m − 1) out of m ToRs send traffic simultaneously to the left 1/m of the ToRs.
Notes: We also investigate the worst-case queue usage of Pyrrha. In a simulation with 1024 hosts and the most stressful workload, Pyrrha’s queue usage is under twenty, which is moderate.

## Slide 107: Conclusion
Pyrrha is a congestion-root-based per-hop flow control, which can control the transmission of flows at a fine granularity without HOL blocking while requiring only a minimal number of queues.
Find our open-source code on: https://github.com/NASA-NJU/Pyrrha
Thanks！
It is time to embrace per-hop flow control to react to congestion promptly！
Notes: Finally, let me make a conclusion.
Pyrrha is a congestion-root-based per-hop flow control protocol, which can control the transmission of flows at a fine granularity without HOL blocking while requiring only a minimal number of queues.
Through Pyrrha, we demonstrate that a head-of-line blocking-free, scalable flow control is feasible. We believe that it is time to embrace per-hop flow control to react to congestion promptly.
// Our codes are publicly available online as a contribution to the research community and to ensure reproducibility.
Thanks for listening.

## Slide 108: Idealized FC can Eliminate HOL blocking but is Non-scalable
Per-flow-queue FC: Vulnerable and background flows fully utilize the link, at the same time the throughput of incast flows does not downgrade.
Notes: To overcome the head-of-line blocking caused by coarse-grained control, an idealized way is per-flow queue flow control, where only queues assigned to congested flows are paused and uncongested flows are unaffected.
As shown by the result, when adopt this method, vulnerable and background flows fully utilize the link, at the same time the throughput of incast flows does not downgrade.

## Slide 109: Simulation Evaluation
Buffer backlog in incast-mix scenario, with or without CC
Pyrrha can avoid congested flows overflow the congestion root and balance the buffer among the switches.
Notes: The detailed analysis on buffer backlog reveals Pyrrha’s ability to manage switch buffer: Pyrrha can avoid congested flows overflow the congestion root and balance the buffer among the switches.

## Slide 110: Pyrrha’s Prototype: Compromise
Pyrrha needs Hierarchical Isolation Queue (HIQ) to handle tree-tangling scenarios.
Although HIQ is supported by some commodity switches [6,7], it is not supported by Tofino2 currently.
[6] (Juniper) Hierarchical class of service overview.
https://www.juniper. net/documentation/us/en/software/junos/cos/topics/ concept/hierarchical-cos-overview.html, 2021.
[7] (Huawei) Introduction to hqos.
https://support.huawei.com/ hedex/hdx.do?docid=EDOC1100168821&id=EN-US_TASK_ 0172371452&lang=en, 2022.

## Slide 111: Pyrrha’s Prototype: Compromise
Fortunately, the features of HIQ can be fully supported via single-tier queues.
P1
P3
P4
P5
Tree-tangling
P2
P6
P8
P9
P7
IQ-P2
IQ-P6
IQ-P2
IQ-P5
IQ-P2&p5
OQ

## Slide 112
Any questions?
Thanks!