## Slide 1
Muhammad Shahbaz
Lalith Suresh, Jennifer Rexford, Nick Feamster,
Ori Rottenstreich, and Mukesh Hira
Elmo
Notes: Hi, my name is Shahbaz. Today, I am going to talk about our work on Elmo, a Source Routed Multicast for Public Clouds. (next slide)

## Slide 2: Elmo: Source Routed Multicast for Public Clouds
Muhammad Shahbaz
Lalith Suresh, Jennifer Rexford, Nick Feamster,
Ori Rottenstreich, and Mukesh Hira
Notes: Hi, my name is Shahbaz. Today, I am going to talk about our work on Elmo, a Source Routed Multicast for Public Clouds. (next slide)

## Slide 3: 1-to-Many Communication in Cloud
Notes: 1-to-many communication is a common communication pattern in cloud workloads, today. (next slide)

## Slide 4: 1-to-Many Communication in Cloud
Streaming Telemetry
State Replication
Distributed Programming
Frameworks
Publish-Subscribe Systems
Infrastructure Applications
and more …
Notes: For example, it’s used in …
(click) streaming telemetry where hosts continuously send telemetry data in incremental updates to a set of collectors,
(click) replication for databases and state machines (e.g., in PAXOS or other consensus algorithms),
(click) distributed programming frameworks (like Spark, and Hadoop),
(click) publish-subscribe systems (like ZeroMQ and RabbitMQ) for publishing messages to multiple receivers,
(click) infrastructure applications (like VMware NSX) running on top of a provider for replicating broadcast, unknown unicast, and multicast traffic.
(click) and more (next slide)

## Slide 5: 1-to-Many Communication in Cloud
10,000s of tenants
100s of workloads
Millions of groups
Notes: And, with cloud providers (like Amazon, Google, and Microsoft) (click) hosting hundreds of thousands of tenants, each with tens to hundreds of such workloads, the number of distinct communications can exceed millions of groups. (next slide)

## Slide 6: 1-to-Many Communication in Cloud
Multicast
10,000s of tenants
100s of workloads
Millions of groups
Notes: The sheer scale of this naturally suggest the use of native multicast, yet none of the data centers enable (next slide)

## Slide 7: 1-to-Many Communication in Cloud
Multicast
10,000s of tenants
100s of workloads
Millions of groups
Notes: it today. (next slide)

## Slide 8: Limitations of Native Multicast
Controller
Notes: Existing approaches to multicast are limited in one or more ways, making them infeasible for cloud deployments. For example,

## Slide 9: Limitations of Native Multicast
Controller
Limited group entries
Excessive control churn
due to membership and topology changes
Processing overhead

## Slide 10: Restricted to Unicast-based Alternatives
S
R
R
Processing
overhead
Controller

## Slide 11: Restricted to Unicast-based Alternatives
Traffic
overhead
Controller
Processing
overhead
S
R
R

## Slide 12: 1-to-Many Communication in the Cloud
Controller
S
R
R

## Slide 13: 1-to-Many Communication in the Cloud
Controller
Traffic
overhead
Processing
overhead
S
R
R

## Slide 14: 1-to-Many Communication in the Cloud
Controller
Excessive control churn
due to membership and topology changes
Processing overhead
Traffic
overhead
Processing
overhead
Limited group entries
S
R
R

## Slide 15: 1-to-Many Communication in the Cloud
Controller
Excessive control churn
due to membership and topology changes
Processing overhead
Traffic
overhead
Processing
overhead
Limited group entries
S
R
R
Need a scheme that scales to millions of groups
without
excessive control, end-host CPU, and traffic overheads!

## Slide 16: Proposal: Source Routed Multicast
Controller
S
R
R

## Slide 17: Proposal: Source Routed Multicast
Controller
S
R
R

## Slide 18: Proposal: Source Routed Multicast
Controller
S
R
R
Negligible
processing overhead
No traffic
overhead
No group entries
needed
Minimal control churn
Little processing overhead
Notes: Ideally, there will be no processing overhead …

## Slide 19: A Naïve Source Routed Multicast
Switch 1: [Ports ]
Switch 2: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
For a data center with:
1000 switches
48 ports per switch
O(30) bytes per switch
O(30,000) bytes header
for a group spanning 1000 switches
20x the packet size!
Switch 3: [.. .. ..]
Switch 5: [.x .. .. ..]
Switch 4: [.. .. .x ..]

## Slide 20: Enabling Source Routed Multicast in Public Clouds
Key attributes:
Efficiently encode multicast forwarding policy inside packets
Process this encoding at hardware speed in the switches
Execute tenants’ applications without modification

## Slide 21: Encoding a Multicast Policy in Elmo
Switch 1: [Ports ]
Switch 2: [.. .. ..]
Switch 5: [.x .. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Switch 3: [.. .. ..]
Switch 4: [.. .. .x ..]

## Slide 22: Encoding a Multicast Policy in Elmo
Switch 1: [Bitmap]
Switch 2: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Switch 3: [.. .. ..]
Switch 5: [.x .. .. ..]
Switch 4: [.. .. .x ..]
Encode switch ports as a bitmap
1
Bitmap is the internal data structure that switches use for replicating packets

## Slide 23: Encoding a Multicast Policy in Elmo
Switch 1: [Bitmap]
Switch 2: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Switch 3: [.. .. ..]
Switch 5: [.x .. .. ..]
Switch 4: [.. .. .x ..]
Group switches into layers
2

## Slide 24: Encoding a Multicast Policy in Elmo
Switch 1: [Bitmap]
Switch 2: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Switch 3: [.. .. ..]
Core
Spine
Leaf
Switch 5: [.x .. .. ..]
Switch 4: [.. .. .x ..]
Group switches into layers
2
Core
Spine
Leaf

## Slide 25: Encoding a Multicast Policy in Elmo
Switch 1: [Bitmap]
Switch 2: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Switch 3: [.. .. ..]
Switch 5: [.x .. .. ..]
Switch 4: [.. .. .x ..]
Switches within a layer with same
ports share a bitmap
3

## Slide 26: Encoding a Multicast Policy in Elmo
Switch 1: [Bitmap]
Switch 2,3: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Core
Spine
Leaf
Switch 5: [.x .. .. ..]
Switch 4: [.. .. .x ..]
Switches within a layer with same
ports share a bitmap
3

## Slide 27: Encoding a Multicast Policy in Elmo
Switch 1: [Bitmap]
Switch 2,3: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Core
Spine
Leaf
Switch 5: [.x .. .. ..]
Switch 4: [.. .. .x ..]
Switches within a layer with same
ports share a bitmap
3
No. of groups
For a data center with:
628 switches
325 bytes header space
Supports 890,000 groups!
Modern commodity switches can parse packet headers of 512 bytes

## Slide 28: Encoding a Multicast Policy in Elmo
Switch 1: [Bitmap]
Switch 2,3: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Core
Spine
Leaf
Switch 5: [.x .. .. ..]
Switch 4: [.. .. .x ..]
Switches within a layer with same
ports share a bitmap
3

## Slide 29: Encoding a Multicast Policy in Elmo
Switch 1: [Bitmap]
Switch 2,3: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Core
Spine
Leaf
Switch 5: [.x .. .. ..]
Switch 4: [.. .. .x ..]
Switches within a layer with N
different ports share a bitmap
4

## Slide 30: Encoding a Multicast Policy in Elmo
Switch 1: [Bitmap]
Switch 2,3: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Core
Spine
Leaf
Switch 4,5:
[.x .. .x ..]
Switches within a layer with N
different ports share a bitmap
4

## Slide 31: Encoding a Multicast Policy in Elmo
Switch 1: [Bitmap]
Switch 2,3: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Core
Spine
Leaf
Switch 4,5:
[.x .. .x ..]
Difference in ports
Switches within a layer with N
different ports share a bitmap
4
No. of groups
For a data center with:
628 switches
325 bytes header space
Supports 980,000 groups!

## Slide 32: Encoding a Multicast Policy in Elmo
Switch 1: [Bitmap]
Switch 2,3: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Core
Spine
Leaf
Switch 4,5:
[.x .. .x ..]
Switches within a layer with N
different ports share a bitmap
4
Fixed Header Size

## Slide 33: Encoding a Multicast Policy in Elmo
Switch 1: [Bitmap]
Switch 2,3: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Core
Spine
Leaf
Switch 4,5:
[.x .. .x ..]
Default Bitmap
Switch Table Entries
Use switch entries and a default
bitmap for larger groups
5
Fixed Header Size

## Slide 34: Encoding a Multicast Policy in Elmo
Fixed Header Size
Default Bitmap
Switch Table Entries
Switch 1: [Bitmap]
Switch 2,3: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Core
Spine
Leaf
Switch 4,5:
[.x .. .x ..]
Switch entries
Difference in ports
Traffic overhead
Use switch entries and a default
bitmap for larger groups
5
For a data center with:
628 switches
325 bytes header space

## Slide 35: Encoding a Multicast Policy in Elmo
Default Bitmap
Switch Table Entries
Switch 1: [Bitmap]
Switch 2,3: [.. .. ..]
A multicast group encoded as
a list of (Switch, Ports) pairs
Core
Spine
Leaf
Switch 4,5:
[.x .. .x ..]
Encode switch ports as a bitmap
Group switches into layers
Switches within a layer with:
- same ports share a bitmap
- N different ports share a bitmap
Use switch entries and a default
bitmap for larger groups
1
5
4
3
2
For a data center with:
628 switches
325 bytes header space
Supports a Million groups!
Fixed Header Size

## Slide 36: Processing a Multicast Policy in Elmo
Controller
1. API
2. Computes the multicast policy
Virtual Switch
S
R
R
3. Installs entries in programmable
virtual switches to push Elmo headers on packets
hardware switches
More flow entries and higher update rates than hardware switches
No changes to the tenant application

## Slide 37: Processing a Multicast Policy in Elmo
Controller
S
R
R
Matching bitmap
or Table entry
or Default bitmap
Switch looks for:

## Slide 38: Applications Run Without Performance Overhead
Subscriber
Publisher

## Slide 39: Conclusion
Designed for multi-tenant data centers
Compactly encodes multicast policy inside packets
Operates at hardware speed using programmable data planes
Elmo
Source Routed
Multicast
for Public Clouds
Learn more here:
https://elmo-mcast.github.io
Notes: In conclusion,
(click)
we presented Elmo, a source-routed multicast service for public clouds. (click) Elmo is designed to be deployable in today’s multi-tenant data centers, while utilizing full bisectional bandwidth of the network. (click) Elmo takes advantage of the unique characteristics of data-center topologies and compactly encodes forwarding rules inside packets and (click) process them at line rate using programmable data planes.
(next slide)

## Slide 41: Backup Slides

## Slide 42: Control Plane Scalability
min (max)
*
*
https://conferences.sigcomm.org/co-next/2013/program/p61.pdf
For a multi-rooted Clos topology with 27K hosts and p-rule header of 325 bytes:
Notes: Elmo reduces control-plane update overhead on network switches and directs updates to hypervisor switches instead. (next slide)

## Slide 43: Elmo Adds Negligible Overheads to Soft. Switches
Notes: Elmo adds negligible overheads to software switches when encapsulating p-rule headers on the packet. Increasing the number of p-rules reduces the pps rate, as the packet size increases, while the throughput in bps remains unchanged which matches the capacity of the links at 20Gbps.
@mshahbaz: maybe talk about how with separate headers, the throughput drops down to about 10Gbps with only 5 p-rules and then tapers off at about 5Gbps with 30 p-rules. (next slide)

## Slide 44: Elmo Operates within the Header Size Limit of Switch ASICs
For a 256-port, 200 mm2 baseline switching ASIC that can parse a 512-byte packet header:
190 bytes for other protocols (e.g., datacenter protocols take about 90 bytes)
Notes: For (click) a 256-port, 200 mm2 baseline switching ASIC that can parse a 512-byte packet header, (click) Elmo consumes only 63.5% of header space even with 30 p-rules, (click) still having 190 bytes for other protocols (e.g., in data-center networks, protocols take about 90 bytes). (next slide)

## Slide 45: Elmo’s Primitives are Inexpensive to Implement in Switch ASICs
For a 256-port, 200 mm2 baseline switching ASIC that can parse a 512-byte packet header:
As a comparison,
Conga consumes 2% of area and
Banzai consumes 12% of area.
Notes: Finally, Elmo’s primitives for bitmap-based output-port selection add only (click) 0.0515% in area costs. This cost is quite modest when compared to CONGA and Banzai schemes that consume an additional switch area of 2% and 12%, respectively. (next slide)