## Slide 1: Offloading Distributed Applications onto SmartNICs using iPipe
Ming Liu, Tianyi Cui, Henry Schuh,
Arvind Krishnamurthy, Simon Peter, Karan Gupta
University of Washington, UT Austin, Nutanix
Notes: Ming’s work

## Slide 2: Programmable NICs
Renewed interest in NICs that allow for customized per-packet processing
Many NICs equipped with multicores & accelerators
  E.g., Cavium LiquidIO, Broadcom Stingray, Mellanox BlueField
Primarily used to accelerate networking & storage
  Supports offloading of fixed functions used in protocols
Can we use programmable NICs to accelerate general distributed applications?
Notes: Compute enabled NICs is an old idea, new lease of life
Dramatic increase in network
Increasing innovation
Broaden, make the leap
low-power and low-cost means

## Slide 3: Talk Outline
Characterization of multicore SmartNICs
iPipe framework for offloading
Application development and evaluation
Notes: Controlled experiments
Informed by the insights and learnings
Performance benefits attainable

## Slide 4: SmartNICs Studied
 | Vendor | BW | Processor | Deployed SW
LiquidIOII CN2350 | Marvell | 2X 10GbE | 12 cnMIPS core, 1.2GHz | Firmware
LiquidIOII CN2360 | Marvell | 2X 25GbE | 16 cnMIPS core, 1.5GHz | Firmware
BlueField 1M332A | Mellanox | 2X 25GbE | 8 ARM A72 core, 0.8GHz | Full OS
Stingray PS225 | Broadcom | 2X 25GbE | 8 ARM A72 core, 3.0GHz | Full OS
Low power processors with simple micro-architectures
Varying level of systems support (firmware to Linux)
Some support RDMA & DPDK interfaces
Notes: Will now describe
Bandwidth
All equipped with multicores with simpler
Though the processor frequency could vary
Emdedded processors

## Slide 5: Structural Differences
Classified into two types based on packet flow
  On-path SmartNICs
  Off-path SmartNICs
Notes: Before I delve
Connectivity of NIC components & how packet flows

## Slide 6: On-path SmartNICs
NIC cores handle all traffic on both the send & receive paths
TX/RX ports
Traffic manager
NIC cores
Host cores
SmartNIC
Notes: NIC cores located between
All packets processed
Active and programmable forwarding

## Slide 7: On-path SmartNICs: Receive path
NIC cores handle all traffic on both the send & receive paths
TX/RX ports
Traffic manager
NIC cores
Host cores
SmartNIC
Notes: TM provides a shared queue
Pull next available packet

## Slide 8: On-path SmartNICs: Send path
NIC cores handle all traffic on both the send & receive paths
TX/RX ports
Traffic manager
NIC cores
Host cores
SmartNIC
Tight integration of computing and communication
Notes: Host signals, NIC core DMAs
Obvious consequence – spend NIC cores
Costs mitigated by tight integration

## Slide 9: Off-path SmartNICs
Programmable NIC switch enables targeted delivery
TX/RX ports
NIC switch
NIC cores
Host cores
SmartNIC
Notes: NIC cores no longer located
Instead, NIC switch for shuttling packets

## Slide 10: Off-path SmartNICs: Receive path
TX/RX ports
NIC switch
NIC cores
Host cores
SmartNIC
Programmable NIC switch enables targeted delivery
Notes: If there is a forwarding rule

## Slide 11: Off-path SmartNICs: Receive path
TX/RX ports
NIC switch
NIC cores
Host cores
SmartNIC
Programmable NIC switch enables targeted delivery

## Slide 12: Off-path SmartNICs: Send path
TX/RX ports
NIC switch
NIC cores
Host cores
SmartNIC
Programmable NIC switch enables targeted delivery
Host traffic does not consume NIC cores
Communication support is less integrated
Notes: handled by the NIC switch in hardware
The resulting symmetric design
aren't tightly integrated with the RX/TX capabilities
NIC communication is less efficient

## Slide 13: Packet Processing Performance
LiquidIO CN2350
Forwarding without any additional processing
Quantifies the default forwarding tax of SmartNICs
Dependent on packet size workload
Notes: Moving on from this qualitative analysis,
perform an empirical analysis

## Slide 14: Processing Headroom
Headroom is workload dependent and only allows for the execution of tiny tasks
Broadcom Stingray
Forwarding throughput as we introduce additional per-packet processing
Notes: impact of introducing packet processing
if the traffic comprises of 1024B packets
can offload only tiny tasks

## Slide 15: Compute Performance
Evaluated standard network functions on the SmartNIC cores
Execution affected by cores' simpler micro-architecture and processing speeds
  Suitable for running applications with low IPC
Computations can leverage SmartNIC's accelerators but tie up NIC cores when batched
  E.g., checksums, tunneling, crypto, etc.
Notes: no standard set of benchmarks
indeed slowed down even after you control
performance boosts from a complex microarchitecture are limited
however means that tasks
while efficiencycould be higher

## Slide 16: Packet Processing Accelerators
On-path NICs provide packet processing accelerators
  Moving packets between cores and RX/TX ports
  Hardware-managed packet buffers with fast indexing
LiquidIO CN2350
Fast and packet-size independent messaging
Notes: Special mention
host x86
In spite of having low speed cores
underscores the benefit

## Slide 17: Host Communication
Non-trivial latency and overhead
  Useful to aggregate and perform scatter/gather
Traverse PCIe bus either through low-level DMA or higher-level RDMA/DPDK interfaces
LiquidIO CN2350
Notes: Finally ... connectivity between the NIC and the host.
latency is about 1.5-2us while the overhead is about 0.5us
Given .. Useful to treat this connection as a communication link that needs to be optimized

## Slide 18: iPipe Framework
Programming framework for distributed applications desiring SmartNIC offload
Addresses the challenges identified by our experiments
Host communication overheads ⇒ distributed actors
Variations in traffic workloads ⇒ dynamic migration
Variations in execution costs ⇒ scheduler for tiny tasks
Notes: set about building a programming framework
addresses the challenges, simultaneously exploiting SmartNIC's capabilities.
views a single node as a distributed system... Lightweight actors
extent of the offload depends on the traffic workloads
handles tiny tasks and providesservice guarantees

## Slide 19: Actor Programming Model
Application logic expressed using a set of actors
Each actor has well-defined local object state and communicates with explicit messages
Migratable actors; supports dynamic communication patterns
Notes: brief overview of the programming model
factoring typically reflecting the fast path and slow path
fairly flexible and powerful model

## Slide 20: Actor Scheduler
Goal is to maximize SmartNIC usage, and
  Prevent overloading and ensure line-rate communications
  Provide isolation and bound tail latency for actor tasks
Theoretical basis:
  Shortest Job First (SJF) optimizes mean response time for arbitrary task distributions
  If the tail response time is to be optimized:
    First come first served (FCFS) is optimal for low variance tasks
    Processor sharing is optimal for high variance tasks
Notes: describe how the system actually adapts to workloads
maximize the utilization of the SmartNIC as a computing substrate without doing no harm.
appropriate scheduling discipline depends on the distribution

## Slide 21: iPipe’s Hybrid Scheduler
Design overview:
  Combine FCFS and deficit round robin (DRR)
    Use FCFS to serve tasks with low variance in service times
    DRR approximates PS in a non-preemptible setting
  Dynamically change actor location & service discipline
    Monitor bounds on aggregate mean and tail latencies
    Profile the mean and tail latency of actor invocations
Notes: Given these properties of scheduling disciplines
Do determine which actors are migrated or transferred

## Slide 22: FCFS Scheduling
NIC FCFS core
NIC DRR core
NIC FCFS core
NIC FCFS cores
NIC DRR core
NIC DRR cores
Shared queue
Host cores
Actors
Tail latency > Tail_threshold
Mean latency > Mean_ threshold
FCFS cores fetch incoming requests from a shared queue and perform run-to-completion execution

## Slide 23: DRR Scheduling
NIC FCFS core
NIC DRR core
NIC FCFS core
NIC FCFS cores
NIC DRR core
NIC DRR cores
Shared queue
Host cores
Actors
Tail latency < (1-⍺) Tail_threshold
Mailbox_len > Q_threshold
DRR cores traverse the runnable queue and execute actor when its deficit counter is sufficiently high
Notes: accumulated enough credits
FCFS cores are operating sufficiently well
fair share of DRR cores is not sufficient

## Slide 24: Applications Built Using iPipe
Replicated and consistent key-value store
Real time analytics
Transaction processing system

## Slide 25: Replicated Key-Value Store
Log-structured merge tree for durable storage
  SSTables stored on NVMe devices attached to host
Replicated and made consistent using Paxos
iPipe realization:
  Memtable/commit log is typically resident on SmartNIC
  Compaction operations on the host

## Slide 26: Evaluation
Application benefits:
  Core savings for a given throughput
  Or higher throughput for a given number of cores
  Latency & tail latency gains
Also in the paper:
  iPipe overheads
  Comparison to Floem
  Network functions using iPipe
  Efficiency of actor scheduler

## Slide 27: Host Core Savings for LiquidIO CN2360
Testbed:
  Supermicro servers, 12-core E5-2680 v3 Xeon CPUs
Offloading adapts to traffic workload
Average reduction in host core count is 73% for 1KB packets

## Slide 28: RKV Store Latency/Throughput (LiquidIO CN2360)
Fixed the host core count and evaluated the improvement in application throughput
2.2x higher throughput and 12.5us lower latency

## Slide 29: Summary
Performed an empirical characterization of SmartNICs
  Significant innovation in terms of hardware acceleration
  Off-path and on-path designs embody structural differences
  SmartNICs can be effective but require careful offloads
IPipe framework enables offloads for distributed applications
  Actor-based model for explicit communication & migration
  Hybrid scheduler for maximizing SmartNIC utilization while bounding mean/tail actor execution costs
Demonstrated offloading benefits for distributed applications

## Slide 30: Hardware Packet Dispatch
Low overhead centralized packet queue abstraction

## Slide 31: iPipe Overheads
Examined non-actor implementation with iPipe version
For the RKV application, iPipe introduces about 10% overhead at different network loads